## Slide 1: Network+ Guide to Networks Eighth Edition
Chapter 4
Network Protocols and Routing
© 2019 Cengage. All Rights Reserved. May not be copied, scanned, or duplicated, in whole or in part, except for use as permitted in a license distributed with a certain product or service or otherwise on a password-protected website for classroom use.

## Slide 2: Objectives
4.1 Describe the functions of core T C P/I P protocols
4.2 Identify how each protocol’s information is formatted in a T C P/I P message
4.3 Explain how routers manage internetwork communications
4.4 Employ various T C P/I P utilities for network discovery and troubleshooting

## Slide 3: T C P/I P Core Protocols (1 of 3)
T C P/I P—A suite of protocols including:
  T C P, I P, U D P, A R P, and many others
T C P/I P protocols add a header to data inherited from the layer above it

## Slide 4: T C P/I P Core Protocols (2 of 3)
Layers 7, 6, and 5—Data and instructions, known as payload, are generated by applications running on source host
Layer 4—A Transport layer protocol, usually T C P or U D P, adds a header to the payload
  Includes a port number to identify the receiving app
Layer 3—Network layer adds it own header and becomes a packet
Layer 2—Packet is passed to Data Link layer on N I C, which encapsulates data with its own header and trailer, creating a frame
Layer 1—Physical layer on the N I C receives the frame and places the transmission on the network

## Slide 5: T C P/I P Core Protocols (3 of 3)
Receiving host de-encapsulates the message at each layer in reverse order and presents payload to the receiving applications
  In transit, transmissions might pass through a number of connectivity devices
Connectivity devices are specialized devices that allow two or more networks or multiple parts of one network to connect and exchange data
  Known by the highest O S I layer they read and process

## Slide 6: T C P (Transmission Control Protocol) (1 of 4)
T C P operates in the Transport layer of O S I model
Three characteristics of T C P:
  Connection-oriented—T C P ensures that a connection or session is established by using a three-step process called a three-way handshake
  Sequencing and checksums—T C P sends a character string called a checksum that is checked by the destination host along with a sequence number for each segment
  Flow control—Gauges rate of transmission based on how quickly recipient can accept data

## Slide 7: T C P (Transmission Control Protocol) (2 of 4)
Fields in a T C P Segment

## Slide 8: T C P (Transmission Control Protocol) (3 of 4)
T C P uses a three-way handshake to establish a connection
  Three transmission sent before data transmission:
    Step 1—Request for a connection (S Y N)
    Step 2—Response to the request (S Y N/A C K)
    Step 3—Connection established (A C K)
  After the three initial messages, the payload or data is sent
  Sequence numbers will be increased by the number of bits included in each received segment
    Confirms the correct length of message was received

## Slide 9: T C P (Transmission Control Protocol) (4 of 4)

## Slide 10: U D P (User Datagram Protocol) (1 of 2)
U D P is an unreliable, connectionless protocol:
  No three-way handshake is performed
  Does not guarantee delivery of data
U D P provides no error checking, sequencing, or flow control
  Makes U D P more efficient than T C P
Useful for live audio or video transmissions over the Internet
Also more efficient for carrying messages that fit within one data packet
A U D P header contains only four fields: Source port, Destination port, Length, and Checksum
  Use of Checksum field in U D P is optional in I P v 4, but required in I P v 6

## Slide 11: U D P (User Datagram Protocol) (2 of 2)

## Slide 12: I P (Internet Protocol) (1 of 4)
I P operates at the Network layer of the O S I model:
  Specifies where data should be delivered
  Identifies the data’s source and destination I P addresses
I P enables T C P/I P to internetwork
  Traverse more than one LAN segment and more than one type of network through a router
I P is an unreliable, connectionless protocol
  Means that I P does not guarantee delivery of data and no session is established before data is transmitted
  I P depends on T C P to ensure messages are put back together in the right order and to ensure each message reaches the correct application on the receiving host

## Slide 13: I P (Internet Protocol) (2 of 4)

## Slide 14: I P (Internet Protocol) (3 of 4)
I P v 6 packets:
  I P v 6 uses a different packet format than I P v 4
  Accommodate the much longer I P v 6 addresses
  There is no Fragment offset field
    I P v 6 hosts adjust their packet sizes to fit the requirements of the network before sending I P v 6 messages

## Slide 15: I P (Internet Protocol) (4 of 4)

## Slide 16: I C M P (Internet Control Message Protocol) (1 of 3)
I C M P is a Network layer, core protocol that reports on the success or failure of data delivery
I C M P can indicate:
  When part of a network is congested
  When data fails to reach its destination
  When data has been discarded because the allotted T T L has expired
I C M P announces transmission failures to the sender
  But does not correct errors it detects
Provides critical information for troubleshooting network problems
I C M P v 6 on I P V 6 networks performs the functions of I C M P and A R P on I P v 4 networks

## Slide 17: I C M P (Internet Control Message Protocol) (2 of 3)

## Slide 18: I C M P (Internet Control Message Protocol) (3 of 3)
Table 4-7 An I C M P packet
Field | Length | Function
Type | 8 bits | Indicates the type of I C M P message, such as Destination Unreachable
Code | 8 bits | Indicates the subtype of the message, such as Destination host unknown
Checksum | 16 bits | Allows the receiving node to determine whether the I C M P packet became corrupted during transmission
Rest of header | 32 bits | Varies depending on message type and subtype
Data | Variable | Usually contains the I P header and first 8 bytes of the data portion of the IP packet that triggered the ICMP message

## Slide 19: A R P (Address Resolution Protocol) on I P v 4 Networks (1 of 4)
A R P works in conjunction with I P v 4 to discover the MAC address of a host or node on the local network
  And to maintain a database that maps IP addresses to MAC addresses on the local network
A R P is a Layer 2 protocol that uses I P in Layer 3
  Operates only within its local network
A R P relies on broadcasting
A R P table—The database of I P-to-MAC address mappings

## Slide 20: A R P (Address Resolution Protocol) on I P v 4 Networks (2 of 4)

## Slide 21: A R P (Address Resolution Protocol) on I P v 4 Networks (3 of 4)
An A R P table can contain two types of entries:
  Dynamic—Created when a client makes an A R P request that could not be satisfied by data already in the A R P table
  Static—Those someone entered manually using the A R P utility (arp command)
To view a Window’s workstation’s A R P table, enter the command:
  arp -a

## Slide 22: A R P (Address Resolution Protocol) on I P v 4 Networks (4 of 4)

## Slide 23: Ethernet (1 of 3)
Ethernet:
  Most important Data Link layer standard
  Capable of running on a variety of network media
  Offers excellent throughput at a reasonable cost
  Most popular network technology used on modern LANs
Ethernet II is the current standard
Adds both a header and a trailer to the payload
  Creates a frame around the payload

## Slide 24: Ethernet (2 of 3)

## Slide 25: Ethernet (3 of 3)
The header and F C S make up the 18-byte “frame” around the data
Data portion of an Ethernet frame may contain from 46 to 1500 bytes
M T U (maximum transmission unit)
  The largest size that routers in a message’s path will allow at the Network Layer
Exceptions to Ethernet frame size limitations:
  Ethernet frames on a V LAN can have an extra 4-byte field between the Source address field and the Type field
  Some special-purpose networks use a proprietary version of Ethernet that allows for a jumbo frame
    The M T U can be as high as 9198 bytes, depending on the type of Ethernet architecture used

## Slide 26: Routers and How They Work (1 of 4)
A router joins two or more networks and passes packets from one network to another
Routers can do the following:
  Connect dissimilar networks (LANs and WANs)
  Interpret Layer 3 and often Layer 4 addressing
  Determine the best path for data to follow from point A to point B
  Reroute traffic if the path of first choice is down but another path is available

## Slide 27: Routers and How They Work (2 of 4)

## Slide 28: Routers and How They Work (3 of 4)
Routers may perform any of the following optional functions:
  Filter broadcast transmissions
  Prevent certain types of traffic from getting to a network
  Support simultaneous local and remote connectivity
  Provide high network fault tolerance through redundant components such as power supplies
  Monitor network traffic and report statistics
  Diagnose internal or other connectivity problems and trigger alarms

## Slide 29: Routers and How They Work (4 of 4)
Router categories:
  Core routers, also called interior routers—Direct data between networks within the same autonomous system (A S)
  Edge routers, or border routers—Connect an autonomous system with an outside network
  Exterior routers—Refers to any router outside the organization’s A S
    Direct data between autonomous systems

## Slide 30: Multilayer Switches
Layer 3 switch—Capable of interpreting Layer 3 data and works much like a router:
  Usually faster and less expensive
  Primary difference is the way the hardware is built
Layer 4 switch—Capable of interpreting Layer 4 data:
  Also known as content or application switches
  Enables switch to perform advanced filtering, keep statistics, and provide security functions
  Typically used as part of a network’s backbone

## Slide 31: Routing Tables (1 of 2)
Routing table—A database that maintains information about where hosts are located and the most efficient way to reach them
  Routers rely on them to identify which router is the next hop to reach a particular destination host
Routing tables contain IP addresses and network masks that identify a network that a host or another router belongs to

## Slide 32: Routing Tables (2 of 2)

## Slide 33: Routing Path Types
Static routing—Network administrators configures a routing table to direct messages along specific paths
  Example—A static route between a small business and its I S P
Dynamic routing—Automatically calculates the best path between two networks and maintains this information in a routing table
  Router can detect problems with failed or congested routes and reroute messages through a different path

## Slide 34: The route Command
The route command allows you to view a host’s routing table:
  On a Linux or UNIX system, use the command route
  On a Windows-based system, use the command route print
  On a Cisco I O S, use the command show ip route

## Slide 35: Routing Metrics
Routing metrics—Properties of a route used by routers to determine the best path to a destination:
  Hop count
  Theoretical bandwidth and actual throughput
  Delay, or latency, on a potential path
  Load, or the traffic or processing burden
  M T U (maximum transmission unit) or the largest I P packet size in bytes allowable without fragmentation
  Routing cost, or a value assigned to a particular route
  Reliability of a potential path
  Topology of a network

## Slide 36: Routing Protocols to Determine Best Paths (1 of 2)
Routing protocols—Used by routers to communicate with each other to determine the best path
Routers rate the reliability and priority of a routing protocol’s data based on these criteria:
  Administrative distance (A D)—A number indicating the protocol’s reliability
  Convergence time—Time it takes to recognize a best path in the event of a change or network outage
  Overhead—The burden placed on the underlying network to support the protocol

## Slide 37: Routing Protocols to Determine Best Paths (2 of 2)
Table 4-10 Summary of common routing protocols
Routing Protocol | Type | Algorithm Used
R I P (Routing Information Protocol) | I G P | Distance-vector
R I Pv2 (Routing Information Protocol, version 2) | I G P | Distance-vector
O S P F (Open Shortest Path First) | I G P | Link-state
I S-I S (Intermediate System to Intermediate System) | I G P | Link-state
E I G R P (Enhanced Interior Gateway Routing Protocol) | I G P | Advanced distance-vector
B G P (Border Gateway Protocol) | E G P | Advanced distance-vector or path vector

## Slide 38: Interior and Exterior Gateway Protocols (1 of 6)
I G P (interior gateway protocols)—Used by core routers and edge routers within autonomous systems and are often grouped according to the algorithms they use to calculate best paths:
  Distance-vector routing protocols—Calculate path on the basis of the distance to that destination
  Link-state routing protocols—Enables routers to communicate beyond neighboring routers in order to independently map the network and determine the best path
E G P (exterior gateway protocols)—Used by edge routers and exterior routers to distribute data outside of autonomous systems
  The only E G P currently in use is B G P

## Slide 39: Interior and Exterior Gateway Protocols (2 of 6)

## Slide 40: Interior and Exterior Gateway Protocols (3 of 6)
O S P F (Open Shortest Path First)—An I G P and a link-state protocol used on interior or border routers
  Introduced as an improvement to R I P
  Characteristics:
    Supports large networks—Imposes no hop limits (unlike R I P)
    Uses a more complex algorithm for determining best paths
    Shared data—Maintains a database of other routers’ links
    Low overhead, fast convergence—Demands more memory and C P U power for calculations, but keeps network bandwidth to a minimum and provides a very fast convergence time
    Stability—Uses algorithms that prevent routing loops
    Multi-vendor routers—Supported by all modern routers

## Slide 41: Interior and Exterior Gateway Protocols (4 of 6)
I S-I S (Intermediate System to Intermediate System)—An I G P and link-state routing protocol:
  Uses a best-path algorithm similar to O S P F
  Is designed for use on core routers only (unlike O S P F)
  Not handcuffed to I P v 4 (like O S P F) so it’s easy to adapt to I P v 6
  Service providers generally prefer I S-I S because it’s more scalable than O S P F

## Slide 42: Interior and Exterior Gateway Protocols (5 of 6)
E I G R P (Enhanced Interior Gateway Routing Protocol)—An advanced distance-vector protocol that combines some of the features of a link-state protocol
  Often referred to as a hybrid protocol
  Fast convergence time and low network overhead
  Easier to configure and less C P U-intensive than O S P F
  Supports multiple protocols and limits unnecessary network traffic between routers
  Originally proprietary to Cisco routers

## Slide 43: Interior and Exterior Gateway Protocols (6 of 6)
B G P (Border Gateway Protocol)—The only current E G P and is known as the “protocol of the Internet”
  Can span multiple autonomous systems
  A path-vector routing protocol that communicates via B G P-specific messages that travel between routers
  Determines the best paths based on many different factors
  Can be configured to follow policies that might avoid a certain router or instruct a group of routers to prefer a particular route
  The most complex of the routing protocols

## Slide 44: Troubleshooting Route Issues
T C P/I P comes with a set of utilities that can help track down most T C P/I P related problems
You should be familiar with the tools and their parameters

## Slide 45: Troubleshooting Tools (1 of 8)
netstat—Displays T C P/I P statistics and details about T C P/I P components/connections on a host
  Information that can be obtained from the netstat command includes:
    The port on which a T C P/I P service is running
    Which network connections are currently established for a client
    How many messages have been handled by a network interface since it was activated
    How many data errors have occurred on a particular network interface

## Slide 46: Troubleshooting Tools (2 of 8)
Table 4-11 netstat command options
netstat command | Description
netstat | Lists all active T C P/I P connections on the local machine, including the Transport layer protocol used, messages sent, and received, I P address, and state of those connections
netstat -n | Lists current connections, including I P addresses and ports
netstat -f | Lists current connections, including I P addresses, ports, and F Q D N s
netstat -a | Lists all current T C P connections and all listening T C P and U D P ports
netstat -e | Displays statistics about messages sent over a network interface, including errors and discards
netstat -s | Displays statistics about each message transmitted by a host, separated according to protocol type (T C P, U D P, IP, or I C M P)
netstat -r | Displays routing table information
netstat -o | Lists the PID (process identifier) for each process using a connection and information about the connection
netstat -b | Lists the name of each process using a connection and information about that connection

## Slide 47: Troubleshooting Tools (3 of 8)
tracert or traceroute
  Windows tracert utility uses I C M P echo requests to trace the path from one networked node to another, identifying all intermediate hops between the nodes
  Linux, UNIX, and O S X systems use the traceroute utility to send U D P messages to a random port on the destination node (concept is the same as tracert)
  Both utilities employ a trial-and-error approach to discover the nodes at each hop from source to destination

## Slide 48: Troubleshooting Tools (4 of 8)

## Slide 49: Troubleshooting Tools (5 of 8)
tracert or traceroute (continued)
  A trace test might stop before reaching the destination for one of three reasons:
    The device the trace is attempting to reach is down
    It’s too busy to process lower-priority messages such as U D P or I C M P
    It does not accept the U D P or I C M P transmissions being sent because a firewall blocks these types of messages
  A trace cannot detect router configuration problems or predict variations of routes over a period of time

## Slide 50: Troubleshooting Tools (6 of 8)
Pathping—A Windows utility that combines elements of both ping and tracert to provide deeper information about network issues along a route
  Sends multiple pings to each hop along a route, then compiles information into a single report
Table 4-13 pathping command options
Pathping command | Description
pathping -n google.com | Instructs the command to not resolve IP addresses to host names
pathping -h 12 google.com | Specifies the maximum number of hops these messages should take when attempting to reach a host
pathping -p 2000 google.com | Identifies the wait time between pings
pathping -q 4 google.com | Limits the number of queries per hop; must be followed by a variable to indicate the number of queries allowed

## Slide 51: Troubleshooting Tools (7 of 8)
tcpdump—A free, command-line packet sniffer that runs on Linux and other Unix O Ss
  Captures traffic that crosses a computer’s network interface
  Output can be saved to a file that you can filter or play back
  You must either use the sudo command or log in as root to access tcpdump

## Slide 52: Troubleshooting Tools (8 of 8)
Table 4-14 tcpdump command options
Tcpdump command | Description
tcpdump not port 22 or tcpdump no port 23 | Filters out S S H or Telnet packets, which is helpful when running tcpdump on a remotely access network device
tcpdump -n | Instructs the command to not resolve I P addresses to host names
tcpdump –c 50 | Limits the number of captured packets to 50
tcpdump -i any | Listens to all network interfaces on a device
tcpdump -D | Lists all interfaces available for capture
tcpdump port http | Filters out all traffic except H T T P
tcpdump -w capture.cap | Saves the file output to a file named capture.cap
tcpdump -r capture.cap | Reads the file capture.cap and outputs the data in the terminal window

## Slide 53: Solving Common Routing Problems (1 of 4)
Table 4-15 Command-line utilities
Command | Common uses
arp | Provides a way of obtaining information from and manipulating a device’s A R P table
dig | Queries D N S servers with more advanced options than nslookup
ipconfig or ifconfig | Provides information about T C P/I P network connections and the ability to manage some of those settings
netstat | Displays T C P/I P statistics and details about T C P/I P components and connections on a host
nmap | Detects, identifies, and monitors devices on a network
nslookup | Queries D N S servers and provides the ability to manage the settings for accessing those servers
pathping (mtr on Linux/UNIX/mac O S) | Sends multiple pings to each hop along a route, then compiles the information into a single report
ping | Verifies connectivity between two nodes on a network
route | Displays a host’s routing table
tcpdump | Captures traffic that crosses a computer’s network interface
traceroute or tracert | Traces the path from one networked node to another, identifying all intermediate routers between the two nodes

## Slide 54: Solving Common Routing Problems (2 of 4)
Duplicate MAC Addresses:
  Two devices on the same network with the same MAC address is a problem
  MAC addresses can be impersonated
    A security risk called spoofing
  Happens most often when managing multiple virtual devices on a large network
  Most switches will detect the problem and produce helpful error messages
    Then it’s a matter of tracking down which virtual devices have the same MAC address and update each device’s configuration

## Slide 55: Solving Common Routing Problems (3 of 4)
Hardware failure—When a router, switch, N I C, or other hardware goes down
  Use tracert or traceroute to track down malfunctioning routers and other devices on larger networks
  Get more accurate trace feedback on a questionable router by targeting a node on the other side of that router, rather than aiming for that router itself
  Use ping to test for network connectivity

## Slide 56: Solving Common Routing Problems (4 of 4)
Discovering neighbor devices—A process used by routers to learn about all of the devices on their networks:
  On I P v 4 networks, neighbor discovery is managed by A R P with help from I C M P
  I P v 6 devices use Neighbor Discovery Protocol (N D P) to automatically detect neighboring devices and automatically adjust when neighboring nodes fail or are removed
    Eliminates the need for A R P and I C M P functions in I P v 6 networks

## Slide 57: Chapter Summary (1 of 3)
T C P/I P is a suite of protocols that includes T C P, I P (I P v 4 and I P v 6), U D P, A R P, and many others
T C P operates at the Transport layer and provides reliable data delivery
U D P is an unreliable, connectionless protocol that provides no delivery guarantees
I P operates at the Network layer of the O S I model and specifies where data should be delivered
I C M P is a Network layer core protocol that reports on the success or failure of data delivery
A R P works in conjunction with I P v 4 to obtain the MAC address of a host

## Slide 58: Chapter Summary (2 of 3)
A router joins two or more networks and passes packets from one network to another
A Layer 3 switch is a switch that is capable of interpreting Layer 3 data and works much like a router
A router relies on its routing table to identify which network a host belongs to and which of the router’s interfaces points toward the best next hop to reach the network
Routing paths are determined by:
  Static routing, which are routes configured by a network administrator
  Dynamic routing, which are routes automatically calculated by the router
The route command allows you to view a host’s routing table

## Slide 59: Chapter Summary (3 of 3)
Routers use routing metrics to determine the best route for messages to take across networks
To communicated with each other, routers use routing protocols that are similar to scouting parties, exploring unknown territories, and collecting data about current network status
Interior gateway protocols are used by core routers and edge routers within an autonomous system
Exterior gateway protocols communicate between autonomous systems
Helpful T C P/I P utilities include ping, ipconfig, ifconfig, nslookup, dig, a r p, route, netstat, tracert, traceroute, pathping, and tcpdump